## Slide 1
UNILAB · DEXTEROUS MANIPULATION
LEAP Hand Dexterous Manipulation
One-Month Research Progress
An evidence chain from model integration and ball caches to sustained rotation and finger gaiting
5
cache tasks
13 reward versions
Reporting period: July 13–28, 2026
Notes: This report reconstructs progress from saved code, configurations, run metadata, TensorBoard diagnostics, and native-viewer inspection.
[Sources]
- D:/UniLab/DEVELOPMENT_LOG.md
- D:/UniLab/logs/rsl_rl_ppo/*/run_config.json
- D:/UniLab/logs/rsl_rl_ppo/*/run_summary.json

## Slide 2
LEAP HAND MONTHLY PROGRESS
From Trainable Environments to Diagnosable Experiments
02
2
MuJoCo / Motrix backend
50k
LEAP-specific ball grasp states
5
independently comparable cache tasks
Core Deliverables
Model and Physics
Imported LEAP assets, dedicated ball/cube scenes, self-collision, and adjacent-link contact filtering.
Reset Distribution
Identified the cube-cache mismatch, built a 50k ball-specific cache, and stored a per-reset anchor.
Research Method
Used checkpoints, task diagnostics, the MuJoCo viewer, and RunIds for controlled reward and curriculum analysis.
Sustained rotation is not yet claimed as solved; the ordering of acquisition, retention, and handoff is now measurable.
Notes: The emphasis is a reliable experimental foundation and traceable evidence, not the highest aggregate reward.
[Sources]
- D:/UniLab/AGENTS.md
- D:/UniLab/DEVELOPMENT_LOG.md

## Slide 3
LEAP HAND MONTHLY PROGRESS
Platform First, Then the Sustained-Rotation Bottleneck
03
7/13–14
Environment
Windows 11 setup, MuJoCo smoke tests, Motrix training, and diagnosis of wgpu OOM recording failures.
7/14–17
LEAP Integration
Imported the hand and dedicated ball/cube assets; added in-hand rotation and toss tasks.
7/17–21
Physics and Cache
Corrected penetration and self-collision behavior; produced the ball-specific 50k reset cache.
7/21–23
Sustained Spin
Created sustained, retention, gaiting, and direct-rotation diagnostic branches.
7/25–28
Simplification
Removed ineffective shaping and converged on the V3-A / V3-B cache-gaiting direction.
Experimental policy: integration smoke test → short diagnostic run → long training only after the direction is supported.
Notes: [Sources]
- D:/UniLab/DEVELOPMENT_LOG.md
- D:/UniLab/AGENTS.md#Dexterous-Manipulation-Training-Guidance

## Slide 4
LEAP HAND MONTHLY PROGRESS
Both Backends Train; Rendering Reliability Differs
04
MuJoCo
• PPO smoke and formal training run successfully
• Native viewer supports checkpoint inspection
• Strong XML, contact, and penetration diagnostics
• Primary backend for current research decisions
Motrix
• Training and interactive playback run successfully
• Intel Arc recording triggered wgpu out-of-memory
• Vulkan and DX12 both closed the render channel
• Retained for backend-contract and performance checks
Decision: use the native MuJoCo viewer for behavioral evidence; do not treat Motrix recording failures as training or physics failures.
Notes: [Sources]
- D:/UniLab/conf/ppo/task/leap_inhand_ball_*/mujoco.yaml
- D:/UniLab/conf/ppo/task/leap_inhand_ball_*/motrix.yaml
- D:/UniLab/DEVELOPMENT_LOG.md

## Slide 5
LEAP HAND MONTHLY PROGRESS
How the Verified 50k Ball Cache Is Generated
05
1
Canonical seed
Use the selected 23-value LEAP ball canonical seed. It survives the full 2.5 s diagnostic with index, ring, and thumb contact and <1 mm penetration.
2
Parallel proposals
Run 1,024 MuJoCo environments. Sample all 16 hand joints within ±0.10 rad, clip to LEAP limits, keep ball-position noise at zero, and disable frontier refinement.
3
Physics settling
Ignore policy output and hold every sampled joint target with PD control for 2.5 s. Production quality gates become active after a 0.5 s warm-up.
4
Recheck and publish
Serialize survivors to float32, reconstruct and recheck them in MuJoCo, deduplicate reset identity at 1 mrad hand / 0.5 mm ball, ignore sphere quaternion, and atomically save exactly 50,000 rows.
Production acceptance gates
Settling gates
• finite, joint limits, and reset height
• anchor drift ≤ 5 mm
• all tip body origins ≤ 100 mm
• ≥ 2 contacts, including thumb
• ball ≤ 0.05 m/s and 0.5 rad/s
• joints ≤ 0.5 rad/s; |work| ≤ 0.25
Serialized-row gates
• contact + thumb repeated
• every tip surface gap ≤ 9.95 mm
• self/object penetration ≤ 1 mm
Published: 50,000 × 23 float32 rows; 50,000/50,000 passed the final static and uniqueness audit.
Notes: The page records the production path used for ball_grasp_official_50k.npy. The final file contains exactly 50,000 unique float32 reset rows; all 50,000 passed the final static audit. SHA-256: 11454e1439cd78efc312028b8fd740d9b125661fd96472b5ca926f3e7dfdc722.
[Sources]
- D:/UniLab/conf/ppo/task/leap_inhand_ball_grasp/mujoco.yaml
- D:/UniLab/src/unilab/envs/manipulation/leap_inhand/ball_grasp_gen.py
- D:/UniLab/src/unilab/assets/robots/leap_hand/caches/ball_grasp_official_50k.npy
[/Sources]

## Slide 6
LEAP HAND MONTHLY PROGRESS
Why the Cache-Rotation Task Branched
06
How to read the map
1 Sustained Cache is the common multi-grasp rotation problem.
2 Finger Gaiting tests whether the first spin stalls because the hand cannot change contacts.
3 V3-A removes complex shaping and returns to an Allegro-style rotation objective.
4 Direct Rotation is supporting evidence: positive rotation can be acquired without a handoff objective.
5 Cache Gaiting V3-B recombines the simplified rotation base with constrained handoff.
Interpretation
The branches are controlled diagnostic experiments, not a linear sequence of task replacements.
Notes: [Sources]
- C:/Users/timli/Downloads/ChatGPT Image 2026年7月28日 下午05_27_48.png
- D:/UniLab/src/unilab/envs/manipulation/leap_inhand/sustained_cache_rotation.py
- D:/UniLab/src/unilab/envs/manipulation/leap_inhand/finger_gaiting_rotation.py
- D:/UniLab/src/unilab/envs/manipulation/leap_inhand/direct_rotation.py
- D:/UniLab/src/unilab/envs/manipulation/leap_inhand/sustained_cache_gaiting_rotation.py

## Slide 7
LEAP HAND MONTHLY PROGRESS
S1–S6: Anchor Helped, but Rotation Still Stalled
07
Last 10% iteration mean · axis speed is EMA
Stage
Effective Run
Reward change
Error
(mm)
Tips
Stage
valid
Axis
EMA
≥2 s
Survival
(s)
S1
07-21 18-22-39
Baseline curriculum
21.83
2.21
16.08%
.0128
.59%
12.06
S2
07-21 22-58-39
+ anchor proximity
19.87
3.05
17.69%
.0137
2.11%
12.14
S3
07-22 02-38-07
+ level spin floor
15.76
3.36
10.56%
.0174
.15%
7.87
S4
07-22 23-04-12
Direct spin; anchor off
18.04
2.23
13.01%
.0161
0%
10.81
S5
07-23 00-19-50
Fixed 0.30 rad/s
14.49
2.57
.07%*
.0255
0%
9.88
S6
07-23 02-40-23
+ continuity penalty
10.06
2.71
.23%*
.0103
0%
8.51
Anchor was the clean win
S1→S2: error −9%, fingertip contacts +38%, and ≥2 s success rose 3.6× with unchanged survival.
Closer did not mean sustained
S3 and S6 pulled the ball closer, but ≥2 s success collapsed and axis speed remained far below the 0.30 rad/s target.
No long-duration solution
No S1–S6 run achieved sustained ≥5 s. *S5–S6 changed stage semantics, so stage-valid is not directly comparable.
Notes: Metrics are arithmetic means over the final 10% of TensorBoard iteration records. S5–S6 use fixed-speed stage semantics and are flagged where direct comparison is unsafe.
[Sources]
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallSustainedCacheRotation/2026-07-21_18-22-39_mujoco
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallSustainedCacheRotation/2026-07-21_22-58-39_mujoco
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallSustainedCacheRotation/2026-07-22_02-38-07_mujoco
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallSustainedCacheRotation/2026-07-22_23-04-12_mujoco
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallSustainedCacheRotation/2026-07-23_00-19-50_mujoco
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallSustainedCacheRotation/2026-07-23_02-40-23_mujoco

## Slide 8
LEAP HAND MONTHLY PROGRESS
S7–S13: Fast Bursts Gave Way to Stable Holding
08
Last 10% iteration mean · axis speed is raw, not EMA · sustained-duration metrics were not logged
Stage
Effective Run
Reward change
Error
(mm)
Tips
Raw axis
(rad/s)
Survival
(s)
S7
07-23 03-57-44
Minimal Allegro-style rotate
—
—
.361
6.79
S8
07-23 15-34-09
+ object linear velocity
—
—
.394
5.53
S9
07-23 20-18-51
+ position error
15.52
1.59
.484
5.62
S10
07-23 21-54-51
+ contact-weighted rotation
17.03
2.86
.384
3.24
S11
07-25 03-50-30
+ support pose / opposition
22.68
1.39
.471
7.00
S12
07-26 23-27-56
V3-A: retention-first gate
6.70
2.75
.030
24.56
S13
07-27 00-36-25
+ gated stall penalty
6.50
1.97
.057
24.67
Contact gating backfired
S9→S10 increased contacts 1.59→2.86, but reduced speed and survival. More contact was not better contact sequencing.
V3-A solved retention
S11→S12 cut error 22.68→6.70 mm and raised survival 7.00→24.56 s, while raw spin collapsed 0.471→0.030.
Stall pressure recovered speed
S12→S13 nearly doubled raw axis speed without harming retention or survival, but duration evidence was still missing.
Notes: Metrics are arithmetic means over the final 10% of TensorBoard iteration records. These runs log raw axis speed, not axis-speed EMA, and do not expose sustained-duration fractions; high raw speed plus short survival is interpreted as burst rotation rather than sustained rotation.
[Sources]
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallSustainedCacheRotation/2026-07-23_03-57-44_mujoco
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallSustainedCacheRotation/2026-07-23_15-34-09_mujoco
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallSustainedCacheRotation/2026-07-23_20-18-51_mujoco
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallSustainedCacheRotation/2026-07-23_21-54-51_mujoco
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallSustainedCacheRotation/2026-07-25_03-50-30_mujoco
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallSustainedCacheRotation/2026-07-26_23-27-56_mujoco
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallSustainedCacheRotation/2026-07-27_00-36-25_mujoco

## Slide 9
LEAP HAND MONTHLY PROGRESS
Anchor Proximity Improved Retention, Not Sustained Rotation
09
RUN Baseline 2026-07-21_18-22-39_mujoco
RUN Grey-zone 2026-07-21_22-58-39_mujoco
Diagnostic
Baseline
+ anchor
Interpretation
anchor position error
23.35 mm
20.09 mm
14% lower; object stays closer to reset anchor
fingertip contacts
2.15
3.00
Stronger enclosure and retention
stage-valid fraction
10.96%
16.22%
+5.26 percentage points of valid states
axis-speed EMA
+0.010
+0.013 rad/s
Only a small gain; still far below target speed
sustained ≥2 s
0.45%
2.16%
Short successes increased but remained rare
sustained ≥5 / 10 s
0% / 0%
0% / 0%
No sustained rotation was acquired
survival seconds
13.11 s
12.78 s
No survival improvement
Conclusion: anchor proximity repaired the 15–30 mm grey zone and improved contact retention, but it did not create long-duration positive angular speed or finger switching.
Notes: [Sources]
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallSustainedCacheRotation/2026-07-21_18-22-39_mujoco/events.out.tfevents.1784683360.沅霆.15996.0
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallSustainedCacheRotation/2026-07-21_22-58-39_mujoco/events.out.tfevents.1784699921.沅霆.13112.0
- D:/UniLab/DEVELOPMENT_LOG.md:2297

## Slide 10
LEAP HAND MONTHLY PROGRESS
Finger Gaiting: Testing Contact Switching
10
Observed failure sequence
Initial push
Brief +Z spin
Contacts freeze
Speed decays to zero
Added rewards and gates
Gaiting term
Weight
stable_support
+0.20
release_progress
+0.05
qualified_handoff
+0.25
A qualified handoff requires
• one finger released for at least 2 control steps
• at least 2 other fingertips remain in contact
• object stays inside the retention gate with no palm contact
• released finger reconnects before timeout and speed recovers
RUN V1 12-19-14 / 12-36-43 V2 14-58-36 / 15-47-22
Notes: [Sources]
- D:/UniLab/src/unilab/envs/manipulation/leap_inhand/finger_gaiting_rotation.py
- D:/UniLab/conf/ppo/task/leap_inhand_ball_finger_gaiting/mujoco.yaml
- D:/UniLab/DEVELOPMENT_LOG.md:2385

## Slide 11
LEAP HAND MONTHLY PROGRESS
Finger Gaiting Exposed Positive Rotation as the Bottleneck
11
RUN 2026-07-22_15-47-22_mujoco
22.33 s
mean survival time
10.48 mm
mean anchor error
2.12
mean fingertip contacts
0.055%
termination rate
The gates that actually failed
Positive speed gate
1.97%
Qualified handoff
< 0.11%
2s / 5s / 10s success
all zero
Interpretation: forcing handoff before reliable positive rotation makes an already sparse exploration problem even harder.
Notes: [Sources]
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallFingerGaitingRotation/2026-07-22_15-47-22_mujoco/run_config.json
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallFingerGaitingRotation/2026-07-22_15-47-22_mujoco/run_summary.json
- D:/UniLab/DEVELOPMENT_LOG.md:2624

## Slide 12
LEAP HAND MONTHLY PROGRESS
Direct Rotation Isolates Basic +Z Acquisition
12
Fixed target: world +Z · 0.30 rad/s · cache reset · 25-second episode · no handoff objective
Positive term
Weight
stable_rotation
+6.0
rotation_streak
+0.5
thumb_contact
+0.1
fingertip_support
+0.15
center_recovery
+1.0
Cost / penalty
Weight
stall
-1.0
reverse
-4.0
object_center
-2.5
object_linear_velocity
-0.4
palm_contact
-1.0
orthogonal_speed
-0.25
failure
-5.0
Direct uses a different reward scale; aggregate return is comparable only among checkpoints from this task.
Notes: [Sources]
- D:/UniLab/conf/ppo/task/leap_inhand_ball_direct/mujoco.yaml
- D:/UniLab/src/unilab/envs/manipulation/leap_inhand/direct_rotation.py
- D:/UniLab/DEVELOPMENT_LOG.md:2620

## Slide 13
LEAP HAND MONTHLY PROGRESS
Direct Acquired Forward Spin, Not Sustained Motion
13
RUN 2026-07-22_21-27-39_mujoco
Rotation acquisition
Task metric
Final value
target +Z speed
0.300 rad/s
axis-speed EMA
+0.246 rad/s
axis purity
84.3%
mean anchor error
14.7 mm
mean fingertip contacts
2.47
palm contact rate
0.0%
Sustainability check
Success gate
Observed fraction
continuous spin ≥ 2 s
0.012%
continuous spin ≥ 5 s
0%
continuous spin ≥ 10 s
0%
natural handoff rate
0.061%
final success fraction
0.061%
Conclusion: the policy can generate positive +Z rotation, but it cannot maintain the motion, switch contacts, or complete multiple turns.
Notes: [Sources]
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallDirectRotation/2026-07-22_21-27-39_mujoco/events.out.tfevents.1784780863.沅霆.41532.0
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallDirectRotation/2026-07-22_21-27-39_mujoco/run_config.json

## Slide 14
LEAP HAND MONTHLY PROGRESS
Cache Gaiting Held Position but Did Not Spin or Handoff
14
V1
Combined the simplified rotation objective with stable-support, release-progress, and handoff shaping.
Problem: gaiting pressure increased exploration cost before stable rotation existed.
RUN 2026-07-27_12-09-05_mujoco
V2
Kept the rotation objective, removed stable/release shaping, reduced handoff influence, and allowed release only for non-thumb fingers.
Goal: acquire rotation first, then require contact switching.
RUN 2026-07-27_12-26-57_mujoco
Latest task metric
Observed value
position gate
98.8%
axis purity
95.1%
axis speed
+0.001 rad/s
net turns / episode
0.0069
speed > 0.10 rad/s
0.73%
qualified handoff rate
0.006%
Interpretation
The object stayed near its anchor and the rotation axis was clean, but axis speed and qualified handoffs were almost zero.
Retention is not sustained rotation.
Notes: [Sources]
- D:/UniLab/conf/ppo/task/leap_inhand_ball_cache_gaiting/mujoco.yaml
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallCacheGaitingRotation/2026-07-27_12-26-57_mujoco/events.out.tfevents.1785180421.沅霆.36252.0
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallCacheGaitingRotation/2026-07-27_12-26-57_mujoco/run_config.json

## Slide 15
LEAP HAND MONTHLY PROGRESS
Each Task Answers a Different Diagnostic Question
15
Task
Representative RunId
Question
Supported conclusion
Evidence
Ball Cache
07-21_17-29-49
Does cache reset work?
Integration is executable
integration only
Sustained Cache
07-21_18-22-39
Can many grasps rotate?
Formal baseline established
rotation metrics
Retention Grey-zone
07-21_22-58-39
Why settle at 15–30 mm?
Retention improved, spin did not
A/B diagnosis
Finger Gaiting
07-22_15-47-22
Is contact switching missing?
Positive speed is the first bottleneck
gate metrics
Direct
07-22_21-27-39
Can forward spin be acquired?
Acquisition is possible but brief
duration metrics
Sustained V3-A
07-27_00-36-25
Can reward be simplified?
Direct task signals retained
reward ablation
Cache Gaiting V2
07-27_12-26-57
Can constrained handoff return?
Retention works; rotation remains absent
task metrics
Historical checkpoints must be interpreted with their saved run_config.json, not the current parent YAML.
Notes: [Sources]
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallCacheRotation/*/run_config.json
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallSustainedCacheRotation/*/run_config.json
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallFingerGaitingRotation/*/run_config.json
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallDirectRotation/*/run_config.json
- D:/UniLab/logs/rsl_rl_ppo/LeapInhandBallCacheGaitingRotation/*/run_config.json

## Slide 16
LEAP HAND MONTHLY PROGRESS
Prove Sustained Rotation Before Reintroducing Handoff
16
Three defensible conclusions
1 A ball-specific reset cache and physically valid collision model are prerequisites.
2 Better retention does not imply sustained rotation; signed axis speed and net angle must be measured.
3 Handoff is eventually necessary, but forcing it before rotation acquisition increases exploration sparsity.
Validation order
01 Reward ablation with fixed cache and seed
02 Report axis-speed duration and net turns
03 Use the viewer to reject palm support or penetration
04 Add handoff only after acquisition is stable
05 Compare success rate across at least three seeds
06 Add domain randomization last
Success criteria
Sustained positive rotation · multiple net turns · low orthogonal speed · no drop · qualified handoff · cross-seed stability
Notes: Maintain a conservative conclusion: the bottleneck is localized, but sustained Cache Gaiting is not yet solved.
[Sources]
- D:/UniLab/AGENTS.md#Dexterous-Manipulation-Training-Guidance
- D:/UniLab/DEVELOPMENT_LOG.md